## Slide 1: Module 6
Implementing Dynamic Host Configuration Protocol
Notes: Presentation: 75 minutes
Lab: 60 minutes
After completing this module, students will be able to:
Install the Dynamic Host Configuration Protocol (DHCP) server role.
Configure DHCP scopes.
Manage a DHCP database.
Secure and monitor the DHCP server role.
Required Materials
To teach this module, you need the Microsoft® Office PowerPoint® file 20410D_06.pptx.
Important: We recommend that you use Office PowerPoint 2007 or a newer version to display the slides for this course. If you use PowerPoint Viewer or an earlier version of Office PowerPoint, all the features of the slides might not display correctly.
Preparation tasks
To prepare for this module:
Read all of the materials for this module.
Practice performing the demonstrations and the lab exercises.
Work through the Module Review and Takeaways section, and determine how you will use this section to reinforce student learning and promote knowledge transfer to on‑the‑job performance.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 2: Module Overview
Overview of the DHCP Server Role Configuring DHCP Scopes Managing a DHCP Database Securing and Monitoring DHCP
Notes: Briefly present an overview of the module.
Reinforce to students that it is important to understand DHCP because many companies implement it, and it is one of the basic networking components in an IT infrastructure.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 3: Lesson 1: Overview of the DHCP Server Role
Benefits of Using DHCP How DHCP Allocates IP Addresses How DHCP Lease Generation Works How DHCP Lease Renewal Works Demonstration: Installing the DHCP Server Role How DHCP Interacts with DNS What Is a DHCP Relay Agent? DHCP Server Authorization
Notes: Briefly present the lesson content.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 4: Benefits of Using DHCP
DHCP reduces the complexity and amount of administrative work by using automatic IP configuration
Automatic IP Configuration | Manual IP Configuration
IP addresses are supplied automatically | IP addresses are entered manually
Correct configuration information is ensured | IP address could be entered incorrectly
Client configuration is updated automatically | Communication and network issues can result
A common source of network problems is eliminated | Frequent computer moves increase administrative effort
Notes: Define DHCP, and explain how it uses automatic IP configuration to reduce the complexity and amount of administrative work that you must perform.
Explain the differences between manual and automatic IP configuration, and provide examples of how it reduces the amount and complexity of administrative work that you must perform.
Instruct students that by using DHCP, they can ensure correct configuration information. However, this is true only if you configure DHCP correctly. If you misconfigure DHCP, clients do not receive the correct configuration from the DHCP server.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 5: How DHCP Allocates IP Addresses
IP Address1: Leased to DHCP Client1
IP Address2: Leased to DHCP Client2
IP Address3: Available for lease
DHCP Client2: IP configuration from DHCP server
Non-DHCP Client: Static IP configuration
DHCP Client1:
IP configuration from DHCP server
Lease generation
Lease
renewal
DHCP database
DHCP server
Notes: Reinforce to students that there are two methods for obtaining a lease: request a new lease or renew an existing one.
Explain that DHCP uses IP broadcasts to initiate communications. Therefore, this limits DHCP servers to communication within their IP subnet. This means that, in many networks, there is a DHCP server for each IP subnet. When this is not feasible, either for cost or management reasons, you can use a DHCP relay agent.
DHCP relay agents listen for client DHCP broadcast packets and send these packets as directed datagrams, or unicast packets, across a router, to a DHCP server on another IP subnet. This makes it possible to maintain a single DHCP server that services multiple IP subnets. You also can use a router that is compatible with Request for Comment (RFC) 1542 to relay DHCP packets into other subnets. Note that on most routers, you must configure this feature before the router actually passes DHCP broadcasts to other subnets. Consult your router’s documentation for details.
A later section of this module provides more details about the DHCP relay agent.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 6: How DHCP Lease Generation Works
DHCP Server2
DHCP Server1
DHCP client
DHCP client broadcasts a DHCPDISCOVER packet
DHCP servers broadcast a DHCPOFFER packet
DHCP client broadcasts a DHCPREQUEST packet
DHCP Server1 broadcasts a DHCPACK packet
Notes: This build slide requires four clicks to see all the slides.
Explain that DHCP uses a four-step process to lease IP addressing information to DHCP clients. Describe the DHCP lease-generation process and refer to the illustrations on the slides.
It is important that students understand this process, so you should run through the demonstration as many times as necessary.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 7: How DHCP Lease Renewal Works
87.5% of lease duration has expired
DHCP client sends a DHCPREQUEST packet
DHCP Server1 sends a DHCPACK packet
If the client fails to renew its lease after 50% of the lease duration has expired, the DHCP lease renewal process begins again after 87.5% of the lease duration has expired
If the client fails to renew its lease after 87.5% of the lease has expired, the DHCP lease generation process starts over again with a DHCP client broadcasting a DHCPDISCOVER
DHCP Server2
DHCP
clients
DHCP Server1
50% of lease duration has expired
100% of lease duration has expired
Notes: This build slide requires three clicks to view all the slides.
Use the graphics on the slide to explain the DHCP lease-renewal process. Mention that DHCP Renewal occurs when 50 percent of lease duration has expired, or during startup, even if more than 50 percent remains. This is because a computer might have been relocated since it was last on the network.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 8: Demonstration: Installing the DHCP Server Role
In this demonstration, you will see how to:
  Install the DHCP server role
  Authorize the DHCP server
Notes: Preparation Steps
Start the following virtual machines:
20410D LON DC1
20410D-LON-RTR
20410D LON SVR1
20410D-LON-SVR2
Demonstration Steps
Install the DHCP server role
Sign in to LON‑SVR1 as Adatum\Administrator with the password Pa$$w0rd.
In Server Manager, in the Manage drop-down menu, click Add Roles and Features.
In the Add Roles and Features Wizard, click Next.
On the Select installation type page, click Next.
On Select destination server page, click Next.
On Select server roles page, select the DHCP Server check box.
In Add Roles and Features Wizard, click Add Features, and then click Next.
On the Select features page, click Next.
On the DHCP Server page, click Next.
On the Confirm installation selections page, click Install.
On the Installation progress page, wait until the “Installation succeeded on lon‑svr1.adatum.com” message appears, and then click Close.
Repeat steps 1 through 11 on LON-SVR2.
20410D
6: Implementing Dynamic Host Configuration Protocol
(More notes on the next slide)

## Slide 9
Notes: Authorize the DHCP Server
On LON‑SVR1, on the Server Manager dashboard, click Tools, and then click DHCP.
In the DHCP console, expand lon‑svr1.adatum.com.
Right‑click lon‑svr1.adatum.com, and then click Authorize.
In the DHCP console, right‑click lon‑svr1.adatum.com, and then click Refresh.
Notice that the icons next to IPv4 and IPv6 change color from red to green, which indicates that the DHCP server has been authorized in Active Directory® Domain Services (AD DS).
5. Repeat steps 1 through 3 on LON-SVR2, replacing the FQDN in step 4 with lon-svr2.adatum.com.
Note: Leave all virtual machines in their current state for the next demonstration.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 10: How DHCP Interacts with DNS
DHCP can:
  Register client records into DNS zones
  Use DNS dynamic update protocol
To use secure DNS dynamic updates, add DHCP servers to the AD DS DnsUpdateProxy global group
DHCP policies:
  Automatically assign settings based on FQDN
  Register workgroup computers with guest DNS suffix
  Disable PTR registrations without disabling host record registration
Notes: While discussing the items on the slide, you might want to show some of the DNS tab configuration items. You can configure various DNS functionality in DHCP, from the DHCP console, by right-clicking the scope name, and then clicking Properties. In the Scope Properties, select the DNS tab. Enable DNS dynamic updates according to the settings below:
Dynamically update DNS records only if requested by the DHCP clients
Discard A and PTR records when lease is deleted
Point out the new (in Windows Server® 2012 R2) check box named Disable dynamic updates for DNS PTR records.
Also, note the Name Protection area. Click the Configure button and point out the text listed there.
Show the various bulleted items under the Enforcing Name Protection window and what will result if they are selected.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 11: What Is a DHCP Relay Agent?
Routers
(non–RFC 1542 compliant)
Subnet A
Subnet B
A DHCP relay agent listens for DHCP broadcasts from DHCP clients and then relays them to DHCP servers in different subnets
DHCP server
DHCP relay agent
DHCP broadcast
DHCP clients
DHCP clients
Unicast
Unicast
Notes: Mention that most routers and most enterprise switches (that can route) support RFC 1542.
The animation requires two clicks to play:
Click one starts the broadcast on Subnet A and the unicast from the relay agent to the server.
Click two starts the unicast from the server to the relay agent and the broadcast on Subnet A.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 12: DHCP Server Authorization
Domain
controller
AD DS
DHCP client
DHCP Server2 checks with the domain controller to obtain a list of authorized DHCP servers
If DHCP Server2 does not find its IP address on the list, the service does not start and support DHCP clients
DHCP client receives IP address
from authorized DHCP Server1
DHCP Server1 checks with the domain controller to obtain a list of authorized DHCP servers
If DHCP Server1 finds its IP address on the list, the service starts and supports DHCP clients
Unauthorized
Does not service DHCP requests
Authorized
Services DHCP requests
DHCP Server1
DHCP Server2
DHCP authorization registers the DHCP Server service in the Active Directory domain to support DHCP clients
Notes: This build slide requires 5 clicks to view all the slides.
Students should understand the importance of DHCP authorization. An unauthorized DHCP server can cause problems in a network, and clients that are configured incorrectly can cause numerous issues, such as an incorrect or duplicate address, a wrong default gateway or DNS server, and a wrong DNS suffix.
Explain that an Enterprise Administrator must authorize installations of a DHCP role in a domain, because several domains can exist in the same IP subnet.
Although we do not recommend it, you can use a stand-alone server as a DHCP server if it is not on a subnet with any authorized DHCP servers. When a stand-alone DHCP server detects an authorized server on the same subnet, it automatically stops leasing IP addresses to DHCP clients.
It is important to note that other non-Microsoft network devices may run DHCP servers. These devices are not able to comply with AD DS authorization, and might cause issues in a networked environment.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 13: Lesson 2: Configuring DHCP Scopes
What Are DHCP Scopes? What Is a DHCP Reservation? What Are DHCP Options? How DHCP Applies Options Demonstration: Creating and Configuring a DHCP Scope
Notes: Briefly introduce the lesson topics to students.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 14: What Are DHCP Scopes?
A DHCP scope is a range of IP addresses that are available to be leased
DHCP scope properties include:
  Network ID
  Lease duration
  Scope name
  Subnet mask
  Network IP address range
  Exclusion range
LAN B
Scope B
LAN A
Scope A
DHCP Server
Notes: Describe the purpose of a DHCP scope.
Explain that administrators must create a DHCP scope before leasing IP addresses to a client.
Instruct students that a scope may contain IP addresses that are not available for lease, and that you configure these addresses as an exclusion. A later module in this course will detail exclusions.
Scope properties contain data about the scope, such as the scope range, the lease duration, DNS update settings, Network Address Protection (NAP) configuration, and DHCP/BOOTP configuration options.
Describe IPv4 or IPv6 scope capabilities.
Explain that you can create scopes by using the New Scope Wizard or Windows PowerShell. Later sections of this module will cover both of these.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 15: What Is a DHCP Reservation?
A DHCP reservation occurs when an IP address within a scope is set aside for use with a specific DHCP client
IP Address1: Leased to Workstation 1
IP Address2: Leased to Workstation 2
IP Address3: Reserved for file and print server
File and print server
Workstation 2
DHCP
server
Subnet A
Workstation 1
Subnet B
Notes: Explain what a DHCP reservation is.
Use the illustration to reinforce that you can configure a DHCP reservation to a file and print server in a different subnet.
Explain why and when you would use a DHCP reservation. For example, if you intend to have network devices, such as network printers, it often is desirable to provide them with a fixed address. This ensures that IP addresses in a predefined scope are not assigned inadvertently to another device, and that if a scope is depleted of addresses, the devices with reservations are guaranteed an IP address.
To configure a reservation, you must know the device’s media access control (MAC) or physical address. This is how the DHCP server knows that the device should have a reservation.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 16: What Are DHCP Options?
DHCP options:
  Are values for common configuration data
  Apply to the server, scopes, reservations, and class options
Common scope options are:
  Router (Default Gateway)
  DNS Name
  DNS Servers
  WINS Servers
Notes: Explain the purpose of DHCP options.
Mention the various DHCP options that you use in Windows-based operating systems deployment, which utilize Preboot Execution Environment (PXE). The PXE requires a DHCP server.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 17: How DHCP Applies Options
You can apply DHCP options at various levels:
  Server
  Scope
  Class
  Reserved client
Typically, you do not apply the class or reserved client options
Notes: Explain how DHCP applies options to client computers when you configure multiple options at the server, scope, class, and reserved-client level. Ensure that students understand that DHCP applies options to client computers in a specific order:
  Server level
  Scope level
  Class level
  Reserved-client level
It also is important that students understand these three points:
Scope options override server options.
Class options override both scope and server options.
Reserved client options apply to devices that have a DHCP reservation.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 18: Demonstration: Creating and Configuring a DHCP Scope
In this demonstration, you will see how to configure scope and scope options in DHCP
Notes: Preparation Steps
You need the 20410D‑LON‑DC1, 20410D‑LON‑SVR1, 20410D‑LON‑RTR, and 20410D‑LON‑SVR2 virtual machines to complete this demonstration. They should be running after the previous demonstration.
Demonstration Steps
Configure scope and scope options in DHCP
On LON-SVR1, in DHCP, in the navigation pane, click lon‑svr1.adatum.com, expand IPv4, right‑click IPv4, and then click New Scope.
In the New Scope Wizard, click Next
On the Scope Name page, in the Name box, type Branch Office, and then click Next.
On the IP Address Range page, complete the page using the following information, and then click Next:
  Start IP address: 172.16.0.100
  End IP address: 172.16.0.200
  Length: 16
  Subnet mask: 255.255.0.0
On the Add Exclusions and Delay page, complete the page using the following information:
  Start IP address: 172.16.0.190
  End IP address: 172.16.0.200
Click Add, and then click Next.
On the Lease Duration page, click Next.
On the Configure DHCP Options page, click Next.
On the Router (Default Gateway) page, in the IP address box, type 172.16.0.1, click Add, and then click Next.
20410D
6: Implementing Dynamic Host Configuration Protocol
(More notes on the next slide)

## Slide 19
Notes: On the Domain Name and DNS Servers page, click Next.
On the WINS Servers page, click Next.
On the Activate Scope page, click Next.
On the Completing the New Scope Wizard page, click Finish.
Configure scope and scope options in DHCP with Windows PowerShell
Explain that you will use similar settings to those that you just applied to LON-SVR1, but you will alter the address range and default gateway for the 10.10.0.0 network, as appropriate.
On LON-SVR2, from the desktop, click the PowerShell icon on the taskbar.
In Windows PowerShell®, type the following cmdlets, and then press Enter after each one:
Add-DhcpServerv4Scope –Name "Branch Office 2" –StartRange 10.10.0.100 –EndRange 10.10.0.200 –SubnetMask 255.255.0.0
Add-Dhcpserverv4ExclusionRange –ScopeID 10.10.0.0 –StartRange 10.10.0.190 –EndRange 10.10.0.200
Set-DhcpServerv4OptionValue –Router 10.10.0.1
Set-DhcpServerv4Scope –ScopeID 10.10.0.0 –State Active
In LON-SVR2 Server Manager, click the Tools drop-down menu, and then select DHCP.
In the DHCP Manager, expand lon-svr2.adatum.com, and then expand IPv4.
Examine the scope that you just created, pointing out the various entries that the Windows PowerShell cmdlets made. Explain that, if you were creating numerous Dynamic Host Configuration Protocol (DHCP) scopes, you could write a Windows PowerShell script by using the cmdlets listed with variables as substitutes for the various IP address that could be called when run.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 20: Lesson 3: Managing a DHCP Database
What Is a DHCP Database? Backing Up and Restoring a DHCP Database Reconciling a DHCP Database Moving a DHCP Database
Notes: Briefly present the lesson content.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 21: What Is a DHCP Database?
Windows Server 2012 stores the DHCP database in the %Systemroot%\System32\Dhcp folder
The DHCP database files include:
The DHCP database is a dynamic database that contains configuration information such as:
  Scopes
  Address leases
  Reservations
  Dhcp.mdb
  temp.edb
  J50.log and J50*.log
  J50Res#####.jrs
  J50.chk
Notes: Describe the DHCP database.
Emphasize that you should not remove or alter the J50.log file, the J50res#####.jrs file, the Dhcp.mdb file, or the tmp.edb file.
Describe compacting the DHCP database.
Ensure that students understand that DHCP databases do not recover space automatically when records are erased. Thus, the database is compacted periodically. If database use increases, it may be necessary to compact it manually. Starting with the Microsoft Windows NT® Server 4.0 operating system, dynamic database compaction occurs on DHCP servers as an automatic background process during idle time or after a database update.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 22: Backing Up and Restoring a DHCP Database
DHCP server
DHCP
Offline storage
The DHCP service automatically backs up the DHCP database to the backup directory on the local drive
If the original database is unable to load, the DHCP service automatically restores from the backup directory on the local drive
The administrator moves a copy of the backed up
DHCP database to an offline storage location
In the event that the server hardware fails, the administrator can restore the DHCP database only from an offline storage location
Back up
Restore
Back up
Restore
DHCP
Notes: This build slide requires five clicks to view all of the slides.
Describe how you back up and restore the DHCP database.
Automatic Backup (Synchronous Backup):
Occurs every 60 minutes.
Best practice: Ensure that you keep an offsite backup of the database.
Best practice: Make sure that your automatic backup is to a different volume than the volume on which your DHCP server is running.
Manual Backup (Asynchronous Backup):
Requires administrative-level permissions. Can also be a member of the DHCP administrators group.
Show students where the option for manual backup is in the console.
What is backed up:
All scopes
Reservations
Leases
All options, including server options, scope options, reservation options, and class options
All registry keys and other configuration settings that are set in DHCP server properties. These settings are stored in the following registry subkey:
  HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\Services\DHCPServer\Parameters
  To back up this subkey, open Registry Editor and then save the specified key to a text file.
Backup Security:
Best Practice: Backups that are stored on another volume should grant permissions only to the administrator and the DHCP administrator groups.
Restore Process:
Requires administrative-level permissions. Can also be a member of the DHCP administrator group.
Note: mention that performing a system state backup of a server that is hosting the DHCP server role results in a backup of the DHCP database and the DHCP server’s configuration.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 23: Reconciling a DHCP Database
Registry | DHCP database | After reconciliation
Client has IP address 192.168.1.34 | IP address 192.168.1.34 is available | Lease entry is created in DHCP database
Summary IP address lease information
Detailed IP address lease information
Compares and reconciles inconsistencies in the DHCP database
DHCP server
DHCP database
Registry
Example:
Notes: Explain how you reconcile a DHCP database.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 24: Moving a DHCP Database
Backup
media
Old DHCP server
New DHCP Server
DHCP
database
DHCP
Database
Steps for moving a DHCP database:
  Back up the DHCP database on the old server
  Stop the old DHCP server service
  Copy the DHCP database to the new server and, if necessary, install the DHCP server role
  Restore the database
  Start the DHCP Server service
Notes: You can move a DHCP database from one server to another by using the normal backup and restore procedure.
Steps for moving a DHCP database:
Back up the DHCP database on the old server.
Stop the old DHCP server service.
Copy the DHCP database to the new server and, if necessary, install the DHCP server role.
Restore the database.
Start the DHCP Server service.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 25: Lesson 4: Securing and Monitoring DHCP
Preventing an Unauthorized Computer from Obtaining a Lease Restricting Unauthorized, NonMicrosoft DHCP Servers from Leasing IP Addresses Delegating DHCP Administration What Are DHCP Statistics? What Is DHCP Audit Logging? Discussion: Common DHCP Issues
Notes: Briefly present the lesson content.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 26: Preventing an Unauthorized Computer from Obtaining a Lease
To prevent an unauthorized computer from obtaining a lease:
  Ensure that unauthorized users do not have physical or wireless access to your network
  Enable audit logging for every DHCP server on your network
  Regularly check and monitor audit log files
  Use 802.1X-enabled LAN switches or wireless access points to access the network
  Configure NAP to validate that a client computer is compliant with system health requirements
Notes: Discuss the guidelines for preventing an unauthorized computer from obtaining a lease.
Emphasize that the only way to prevent unauthorized access completely by using only DHCP is to disallow network access. However, this is not feasible. Therefore, the next best actions are to limit the possibility of an unauthorized user plugging into an empty network jack by implementing security on a wireless network.
Use NAP to validate a client computer’s health. NAP can determine if the computer is running an up‑to‑date antivirus program and has the latest Windows operating system updates. If the computer is not compliant with the NAP policy, it can be denied network access or relegated to a remediation network where it can obtain the necessary updates to become compliant.
You also can use NAP to restrict access to a network based on whether the user is authorized for network access.
Some organizations lock down the network ports based on MAC address. Each MAC address is restricted to a specific port. If a different MAC address attempts to communicate on that port, the port will shut down.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 27: Restricting Unauthorized, NonMicrosoft DHCP Servers from Leasing IP Addresses
DHCP clients
Unauthorized DHCP server
Legitimate DHCP server
To eliminate an unauthorized DHCP server, you must locate it and then either physically disable it or disable the DHCP service, to prevent it from communicating on the network
Notes: Mention to students that users must disable DHCP services from other devices, such as routers or non‑Microsoft tools.
If users complain of network access problems, check the IP settings that the DHCP server is providing by using the ipconfig /all command.
If the DHCP server result is not correct, investigating the IP address in question should identify the problem.
The only way to restrict unauthorized DHCP servers is to find their source IP, and then to remove them from the network.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 28: Delegating DHCP Administration
To delegate who can administer the DHCP service:
  Limit the membership of the DHCP Administrators group
  Add users to the DHCP Users group if they need read-only access to the DHCP console
Account | Permissions
DHCP Administrators group | Can view and modify any data about the DHCP server
DHCP Users group | Has read-only DHCP console access to the server
Notes: 20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 29: What Are DHCP Statistics?
DHCP statistics are collected at either the server level or the scope level
DHCP Server
Server Statistics window
Notes: Explain that DHCP statistics provide a general view of DHCP activity and usage.
Point out that you can configure the statistics’ refresh rate in the General tab of the server’s Properties dialog box.
Show students the statistics panel in the DHCP Server.
For the DHCP server statistics section
Provide an overview of DHCP server usage. Point out to students that they can use this data to understand the DHCP server’s state quickly.
For the DHCP scope statistics section
Provide basic data about the leases in the DHCP scope.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 30: What Is DHCP Audit Logging?
Notes: Describe the purpose of the DHCP audit log.
Explain that the DHCP audit log file is stored in systemroot\system32\dhcp, and that the name of the audit log file is based on the day of the week it was created. For example, if the day of the week is Monday, then the file name is DhcpSrvLog‑Mon.log.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 31: Discussion: Common DHCP Issues
10 minutes
Common issues that can occur when you do not configure DHCP properly:
  Address conflicts
  Failure to obtain a DHCP address
  Address obtained from an incorrect scope
  DHCP database suffered data corruption or loss
  DHCP server has exhausted its IP address pool
Notes: Discuss common issues that can occur when you do not configure DHCP properly.
For each of the issues, ask students:
What tests, tools, and procedures would they use to troubleshoot the issue?
What is the cause of the issue?
What would they consider as a solution?
Each student should write in the empty space of the table in the Student Handbook what the possible cause of the issue might be, and their proposed solution.
Some suggested answers to aid the discussion:
Address conflicts:
  Check for manually configured computers with a conflicting address.
  Verify that scopes do not contain overlapping addresses.
  Inform students that you can configure a DHCP server to ping an IP address before it leases it, which helps prevent conflicts.
Failure to obtain a DHCP address:
  Verify that the DHCP server is online.
  Verify connectivity to the subnet containing the DHCP server.
  Verify that there are sufficient addresses in the address pool.
Address obtained from incorrect scope:
  Check other clients in the subnet for their configuration.
DHCP database suffers data corruption or loss:
  Restore or recreate the DHCP database.
DHCP server exhausts its IP address pool:
  Reduce the lease duration.
  Consider redesigning the IP address pools.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 32: Lab: Implementing DHCP
Exercise 1: Implementing DHCP Exercise 2: Implementing a DHCP Relay Agent (Optional Exercise)
Logon Information
Virtual machines 20410D‑LON‑DC1
20410D‑LON‑SVR1
20410D‑LON‑RTR
20410D‑LON‑CL1
20410D‑LON‑CL2
User name Adatum\Administrator
Password Pa$$w0rd
Estimated Time: 60 minutes
Notes: Before the students begin the lab, read the lab scenario and display the next slide. Before each exercise, read the scenario associated with the exercise to the class. The scenarios give context to the lab and exercises, and help to facilitate the discussion at the end of the lab. Remind students to complete the discussion questions after the last lab exercise.
Exercise 1: Implementing DHCP
As part of configuring the infrastructure for the new branch office, you need to configure a DHCP server that will provide IP addresses and configuration to client computers. Servers are configured with static IP addresses and usually do not use DHCP for obtaining IP addresses.
One of the client computers in the branch office needs to access an accounting app in the head office. The network team uses firewalls based on IP addresses to restrict access to this app. The network team has requested that you assign a static IP address to this client computer. Rather than configuring a static IP address on the client computer manually, you decide to create a reservation in DHCP for the client computer.
Exercise 2: Implementing a DHCP Relay Agent (Optional Exercise)
To avoid configuring an addition DHCP server on the subnet, your manager has asked you to configure a DHCP relay agent for another subnet in your branch office.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 33: Lab Scenario
A. Datum Corporation has an IT office and data center in London, which supports the London location and other locations as well. A. Datum has recently deployed a Windows 2012 Server infrastructure with Windows 8 clients.
You have recently accepted a promotion to the server support team. One of your first assignments is to configure the infrastructure service for a new branch office. As part of this assignment, you need to configure a DHCP server that will provide IP addresses and configuration to client computers. Servers are configured with static IP addresses and do not use DHCP.
Notes: 20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 34: Lab Review
What purpose does the DHCP scope have? How should you configure a computer to receive an IP address from the DHCP server? Why do you need MAC address for a DHCP server reservation? What information do you need to configure on a DHCP relay agent?
Notes: Lab Review Questions
Question
What purpose does the DHCP scope have?
Answer
The DHCP scope defines what information is leased to DHCP clients through the DHCP process, such as the IP address, the subnet mask, the DNS server IP address, and the Default Gateway IP address.
Question
How should you configure a computer to receive an IP address from the DHCP server?
Answer
You should not have to do anything. The computer should be configured to obtain its IP address automatically.
Question
Why do you need MAC address for a DHCP server reservation?
Answer
The MAC address uniquely identifies a computer or any other network device, such as network printer. The DHCP reservation process needs to identify the computer or the network device through the MAC address, so it can lease an IP address to the computer or network device.
Question
What information do you need to configure on a DHCP relay agent?
Answer
For a DHCP relay agent to provide IP addresses for subnets that have no DHCP server installed, you need to install DHCP relay agent protocol on a server that will act as a DHCP relay agent. In addition, you must configure the DHCP relay agent to contact the IP address of the DHCP server in another subnet, for purposes of leasing IP addresses to DHCP clients.
20410D
6: Implementing Dynamic Host Configuration Protocol

## Slide 35: Module Review and Takeaways
Review Questions Best Practices
Tools
Notes: Module Review Questions
Point the students to the appropriate section in the course so that they are able to answer the questions that this section presents.
Question
You have two subnets in your organization. You want to use DHCP to allocate addresses to client computers in both subnets, but you do not want to deploy two DHCP servers. What factors must you consider?
Answer
Either the router that interconnects the two subnets must support DHCP relaying, or you must place a DHCP relay agent on the subnet that does not host the DHCP server. Additionally, you should consider the impact on service availability in case the single DHCP server fails.
Question
Your organization has grown, and your IPv4 scope is almost out of addresses. What should you do?
Answer
Consider redesigning your IPv4 scope.
Question
What information do you require to configure a DHCP reservation?
Answer
You require the MAC address of the client that will lease the reservation.
Question
Can you configure option 003 – Router as a Server-level DHCP scope option?
Answer
Yes, but you should configure the option in each subnet. In a multi-subnet environment, all clients from the same subnet should obtain the same gateway setting.
20410D
6: Implementing Dynamic Host Configuration Protocol
(More notes on the next slide)

## Slide 36
Notes: Best Practices
Discuss best practices and real-world scenarios with students, and ask for their experience with the topics shown.
The following are some best practices that students can follow:
Design your IP addressing scheme carefully so that it accommodates the requirements of both your current and future IT infrastructure.
Determine which devices need DHCP reservations, such as network printers, network scanners, or IP-based cameras.
Secure your network from unauthorized DHCP servers.
Configure the DHCP database on highly available disk drive configurations, such as a redundant array of independent disks (RAID)‑5 or RAID‑1, to provide DHCP service availability in case of a disk failure.
Back up the DHCP database regularly. Test the restore procedure in an isolated, non‑production environment.
Monitor the system utilization of DHCP servers. Upgrade the DHCP server hardware if necessary to provide better service performance.
Tools
20410D
6: Implementing Dynamic Host Configuration Protocol
Tool | Use for | Where to find it
DHCP | Graphical User Interface for managing DHCP Server | Server Manager
Windows PowerShell | Command-line interface for managing DHCP Server | Windows taskbar on the desktop
Ipconfig.exe | Managing and troubleshooting client IP settings | Command line
Netsh.exe | Configuring both client and server‑side IP settings, including those for DHCP server role | Command line
Regedit.exe | Editing and fine‑tuning settings, including those for the DHCP server role | Windows interface or Command line